Lime Microsystems Limited

Surrey Technology Centre
Occam Road
The Surrey Research Park
Guildford, Surrey GU2 7YG
United Kingdom

Tel:	+44 (0) 1483 685 063
Fax:	+44 (0) 1428 656 662
e-mail:	enquiries@limemicro.com

STREAM Development kit
 User Guide

- User Guide for Linux OS Installation -

REVISION HISTORY

The following table shows the revision history of this document:

Date	Version	Description of Revisions
27/02/2015	1.0	Initial version
03/04/2015	1.1	Added document licence info (Creative Commons Attribution 3.0 Unported)

Table of Contents

Table of Figures

# Requirements

Required Software:
- CyControl (Cypress USB control center)
- OpenOCD (>=0.8.0)
- Tera Term
- Zadig

Required Hardware:
- Altera USB Blaster
- 3.3V USB-to-Serial cable
- USB A to microB cable

Current manual describes how to load Linux image to FPGA via FX3 controller.
Information regarding software architecture and links to source codes are available in \Stream\stream_openrisc_soc_v2\doc directory.

# Step by step instructions

## Step 1. Installing USB drivers

Use J2 USB3.0 to connect to PC.
To install Cypress FX3 USB3.0 (IC6) drivers navigate driver installer to \Stream\Stream_LMS7EVB_distro_05v\fx3\drivers\bin\

## Step 2. Load FX3 firmware

Run CyControl from \Stream\Stream_LMS7EVB_distro_05v\fx3\software
Press Program → FX3 → RAM → navigate to …\fx3\firmware_img\usb_trx_V2 → Open.
“Cypress USB BootLoader” should change to “Cypress USB StreamerExample”.

Figure . CyControl Cypress USB StreamerExample should appear

## Step 3. LMS7Suite for FPGA programming

Run LMS7Suite from \Stream\Stream_LMS7EVB_distro_05v\gui directory.
Go to Options → Connection Settings → Cypress USB StreamerExample (Stream) → OK
Now connection between FX3 controller and PC is set.
Now it is time to load RISC architecture in to FPGA: go to Programming section. Press Open and navigate to \Stream\stream_openrisc_soc_v2\bin\stream.rbf. Press Program.

Figure . FPGA programming via LMS7Suite
## Step 4. Serial connection setup
Connect 3.3V USB-to-Serial cable to J1 (FPGA GPIOs header).
Pin 1: FPGA RX pin (orange)
Pin 3: FPGA TX pin (yellow)
Pin 10: GND (black)
Establish connection using Tera Term via Serial Port.

Figure . Tera Term Serial Port setup
FPGA is not ready yet, so Terminal window is empty.

## Step 5. Altera USB Blaster

Connect Altera USB Blaster to J23 FPGA JTAG header.
Install USB-Blaster driver using Zadig.
Run Zadig → Options → List All Devices. Select USB-Blaster and libusbK driver.

Figure . Zadig driver installer

## Step 6. OpenOCD installation

Install OpenOCD.
Copy vmlinux (Linux image) from \stream_openrisc_soc_v2\bin to OpenOCD installation directory C:\Program Files\GNU ARM Eclipse\OpenOCD\bin
Run Windows Command Prompt.
Change current directory to OpenOCD installation directory:
cd C:\Program Files\GNU ARM Eclipse\OpenOCD\bin
Launch OpenOCD with:
Openocd –f interface/altera-usb-blaster.cfg –f board/or1k_generic.cfg

Figure . Launching OpenOCD

## Step 7. Installing Linux

Turn ON Windows Telnet (Control Panel → Programs → Turn Windows features on or off)
Open a new Command Prompt window and connect to the OpenOCD proxy with telnet localhost 4444.
Run the following command to load the Linux image halt; load_image vmlinux; reg npc 0x100; reset.

Figure . Loading Linux image
The Linux boot process should now start in the terminal connected to the serial console.
After the boot is complete you should be greeted by a message saying Please press Enter to activate this console.
Press Enter and you can start using Linux commands.

Figure . Linux loading completed